### Flood forecasting

Flash-Flood sub-case proposal

(Flash flood urban warning integrated system

based on ESPADA tool operational since 2005)

- Narrative explanation

The Mediterranean urban areas are often crossed by many small rivers or “caderaux”. This complex hydrographic network is most of the time absolutely dry, but potentially fed by large karstic watersheds around the cities.

Often at the end of the summer and in the autumn,  heavy and almost stationary thunderstorms occurs (called “V supercells” fed by the still warm waters of the sea and early cold air advections at upper levels) resulting in a sudden overflow of the network  and catastrophic flooding over some neighbourhoods and sometimes whole the towns.

In collaboration with public and private organizations, the city of Nîmes operates an integrated  real-time urban flash flood management tool that combines current technologies for measurement, telecommunications and hydrographic models.

The system includes :

- A network of ground sensors (measures of rainfall accumulation and discharges)

- A network of radars  (real-time rainfall accumulation and intensity)

- A nowcasting  system for rainfall accumulation (based on observed radar data and  2PIR method)

- 1D runoff hydrographic models (GR4 and RERAM)

- A statistical  model  (based on past events) to identify the probable flood scenario, because it is not possible to run (in real time) a 2D flood model to simulate the stream across the streets after overflow of  the storm drainage network  (too CPU time consuming regarding the emergency response time scale)

- Visualization systems (meteorological data )

- Cameras placed on a few strategic locations supplement these observations.

- Alert Systems

- High level Use-Case

| Use Case Description |
| --- |
| Name | Flash flood urban warning integrated system |
| Priority | High |
| Description | Real-time urban flash flood management tool |
| Pre-condition | Meteorological situation conducive to heavy and almost stationary thunderstorms (“V supercells”) |
| Flow of Events – Basic Path |
| Step 1 | acquisition of real-time observed data ( discharges, rainfall amount from surface sensors and radars) Acquisition of short-term forecast for rainfall accumulations |
| Step 2 | Process the data in real-time to simulate and forecast the discharges : Hydrographical model (GR4) upstream the urban area, and another model for the urban area itself (RERAM) |
| Step 3 | Automated identification of the flood scenario which most likely corresponds to the expected discharges (simulated) and past events. |
| Step 4 | Visualize the results (real-time data, model output, risk map) Human assessment of the risk facing the flooding scenario |
| Step 5 | Ignition of the warning plan depending on the risk |

#### Overview of watersheds (dark green) , surface sensors : rain gauges and discharges gauges

#### Nîmes  (Gard, France)

#### Overview of watersheds (dark blue)  and areas of interest  for radar accumulations  (almost-rectangular areas)

#### Nîmes  (Gard, France)

Overview of the resulting risk map over an urban area

Nîmes (Gard, France)

- Detailed Use-Case Diagram

The initial use-case has been split  in order to isolate sub-cases related to the INSPIRE themes “Atmospheric Conditions” and “Meteorological Geographical Features” .  Hydrology is actually the business core of this use-case, the meteorological sub-cases are intended to provide weather data (essentially rainfall accumulation observations and very short-range forecasts – “nowcasting”).

Meterological  4 sub-cases would be  :

- Visualize real-time meteorological data  to assess the meteorological situation and how it evolves. At least :

  - Radar data (rainfall accumulations and intensity)

  - Surface observations (rainfall accumulations)

  - Nowcasting (rainfall accumulations)

Ideally :

  - All data related to convective cell activity ( lightning, satellite imagery - especially IR bands, cell track,  fine mesh non-hydrostatic models)

- Retrieve observed rainfall data  for visualisation, and as input of the hydrological “runoff”f model

  - Radar data (accumulations, basin accumulation,  intensity)

  - Surface observations (rainfall accumulations)

- Retrieve rainfall nowcasting data for visualisation and as input of the runoff model

  - Rainfall accumulation over a watershed (based on radar data)

- Retrieve meteorological data from past events in order to calibrate the hydrological models

  - Observed radar data (rainfall accumulation)

  - Surface observations (rainfall accumulations)

- Detailed structured description of meteorological sub-cases (mainly data accès)

| Use Case Description |
| --- |
| Name | Retrieve observed rainfall data |
| Priority |  |
| Description | Information type : Surface observation (point, point series) Radar data (imagery, gridded data) Radar data (rainfall amount over a domain) |
| Pre-condition |  |
| Flow of Events – Basic Path (Data queries) |
|  | Catalog access Query AvailableDatasets phenomenon [rainfall accumulation, rainfall intensity] areaOfInterest [BBOX] temporalExtent [Period] ) Note : The semantics of temporalExtent is that of samplingTime (or phenomenonTime) in O&M (OGC Observations & Measurements) |
|  | Data access Query SurfaceObservation dataType [point, pointSeries] phenomenon [rainfall accumulation 5’,15’,30’,60’] areaOfInterest [BBOX , Polygon] temporalExtent [Period, Instant, default=Last] Notes : - the accumulation period is part of the phenomenon |
|  | Data access Query RadarData dataType [gridFeature, gridSerieFeature, scanningRadarFeature, (imagery)] phenomenon [rainfall accumulation 15’,30’,60’] areaOfInterest [BBOX] temporalExtent [Period, Instant, default=Last] |
|  | Data access Query RadarData ( dataType [gridFeature, gridSerieFeature, scanningRadarFeature, (imagery)] phenomenon [rainfall intensity, reflectivity] areaOfInterest [BBOX] temporalExtent [Period, Instant, default=Last] |
|  | Data access Query RadarData dataType [point, pointSeries] phenomenon [rainfall accumulation 15’,30’,60’] areaOfInterest [Polygon] temporalExtent [Period, Instant, default=Last] Note : - integrated amount of rainfall over a domain (basin) defined by a polygon |
| Flow of Events – Alternative Path |
|  | none |
| Data source : Surface observation |
| Description | Rainfall amount (accumulation) for a time period, from a network of sensors Area of interest : ~100 Km2 (whole system domain) Time range for accumulation : 5’ 6’ 15’ 30’ 60’ Update frequency : 1’ 5’ (6’) Number of platforms (stations) : ~30 |
| DataProvider | NMHS, other private operator networks |
| GeographicScope | Limited area - system domain ~100 Km2 |
| ThematicScope (INSPIRE) | Atmospheric Conditions, Meteorological Geographical features |
| Scale, resolution | Discrete data (~30 stations ) |
| Delivery | XML (GML) or BUFR encoding |
| Documentation |  |
| Data source : 2 D radar rainfall amount (accumulation) |
| Description | 2D radar rainfall amount (accumulation) Area of interest : ~100 Km2 (whole system domain) Time range for accumulation : 15’ 30’ 60’ Update frequency : 5’ |
| DataProvider | NMHS (National Meteorological and Hydrological Service) |
| GeographicScope | Limited area - system domain ~100 Km2 |
| ThematicScope | Atmospheric Conditions, Meteorological geographical features |
| Scale, resolution | Resolution : 1 km. |
| Delivery | GRIB, GeoTiff |
| Documentation | Data is self-documented |
| Data source : 2D radar rainfall intensity |
| Description | 2D radar rainfall intensity (Kg/m2/h) or reflectivity (DBZ) Area of interest : ~100 Km2 (whole system domain) Update frequency : 5’ |
| DataProvider | NMHS |
| GeographicScope | Limited area - system domain ~100 Km2 |
| ThematicScope | Atmospheric Conditions, Meteorological geographical features |
| Scale, resolution | Resolution : 1 km. |
| Delivery | GRIB, GeoTiff |
| Documentation | The data is self-documented |
| Data source : 0D radar rainfall amount over an area of interest |
| Description | Integrated rainfall amount (kg) over a watershed (polygon) Area of interest : Few km2 Update frequency : 5’ |
| DataProvider | NMHS |
| GeographicScope | Limited area : hydrographic basin, hydrographic model domain, other area of interest |
| ThematicScope | Atmospheric Conditions, Meteorological geographical features |
| Scale, resolution | Resolution : Discrete data (one point per area of interest) |
| Delivery | XML |
| Documentation | The data is self-documented |

| Use Case Description |
| --- |
| Name | Retrieve rainfall nowcasting data |
| Priority |  |
| Description | Information type : Radar based forecast (imagery, gridded data) Radar based forecast (rainfall amount over a watershed) Very short range forecast : max offset 90’ |
| Pre-condition |  |
| Flow of Events – Basic Path (Data queries) |
|  | Catalog access Query AvailableDatasets phenomenon [rainfall accumulation forecasts] areaOfInterest [BBOX] temporalExtent [Period] ) |
|  | Data access Query RadarBasedForecast dataType [gridFeature, gridSerieFeature, (imagery)] phenomenon [rainfall accumulation 15’,30’,60’] areaOfInterest [BBOX] analysisTime [Instant, default=Last] temporalExtent [Period, Instant, default=Last] |
|  | Data access Query RadarBasedForecast dataType [point, pointSeries] phenomenon [rainfall accumulation 15’,30’,60’] areaOfInterest [Polygon] analysisTime [Instant, default=Last] temporalExtent [Period, Instant, default=Last] Note : integrated amount of rainfall over a watershed defined by a polygon forecast offset max : 90’ |
| Flow of Events – Alternative Path |
|  | none |
| Data source : 2 D rainfall amount forecast (radar based) |
| Description | radar rainfall amount (accumulation) Area of interest : ~100 Km2 (whole system domain) Time range for accumulation : 15’ 30’ 60’ Max forecast offset : 90’ Update frequency : 5’ |
| DataProvider | NMHS (National Meteorological and Hydrological Service) |
| GeographicScope | Limited area - system domain ~100 Km2 |
| ThematicScope | Atmospheric Conditions, Meteorological geographical features |
| Scale, resolution | Resolution : 1 km. |
| Delivery | GRIB, GeoTiff |
| Documentation | Data is self-documented |
| Data source : 0D rainfall amount forecast over an area of interest |
| Description | Integrated rainfall amount (kg) forecast over a watershed (polygon) Area of interest : Few km2 Time range for accumulation : 15’ 30’ 60’ Max forecast offset : 90’ Update frequency : 5’ |
| DataProvider | NMHS |
| GeographicScope | Limited area : hydrographic basin, hydrographic model domain, other area of interest |
| ThematicScope | Atmospheric Conditions, Meteorological geographical features |
| Scale, resolution | Resolution : Discrete data (one point per area of interest) |
| Delivery | XML |
| Documentation | The data is self-documented |

| Use Case Description |
| --- |
| Name | Retrieve data from past events |
| Priority |  |
| Description | Information type : Surface observation (point, point series) Radar data (imagery, gridded data) The query model is the same as for real-time data |
| Pre-condition |  |
| Flow of Events – Basic Path (Data queries) |
|  | Note : the query model is the same as those for real-time observed data, but the data source (at Meteo-France…) is not the same |

# References

- Chocat  B., “Encyclopédie de l’hydrologie urbaine et de l’assainissement“, Lavoisier, Paris, 1124  pages (1997).

- Dumay H. et Raymond M., “ ESPADA : Un outil pour la gestion des crues urbaine“, Conférence Novatech Lyon (2001).

- Editjano et Michel, C., “Un modèle pluie-débit journalier à trois paramètres“, La Houille Blanche, 2, 11"-121 (1989).

- Maréchal.J.C., Ladouche.B. et Doerfliger.N. ,  “Role of karst system in the genesis of flash flood  events at the Nîmes city“, in EGU, Vienne , Autriche (2-7 avril 2006)

- Perrin  C., “Vers une amélioration d'un modèle global pluie-débit au travers d'une approche comparative“, Thèse  INP CEMAGREF (2000).

- Raymond M., Peyron N. et Martin A. “ESPADA, “ A unique flood management tool: first feedback  from the September 2005 flood in Nimes”, 7th International Conference on Hydroinformatics, Nice, France (2006).

# Text boxes

1 Km Km

# Rainfall gauges

# Discharges gauges