Open Geospatial Consortium

Date: 2012-??-??

External identifier of this OGC® document: <http://www.opengis.net/doc/template/standard/1.0>

Internal reference number of this OGC® document: 12-nnnr1

Version: 0.3.0

Category: OGC® Best Practice

Editor: <Name(s) of Editor or Editors>

Best Practices for using OGC WMS with Time-Dependent or Elevation-Dependent Data

Copyright notice

Copyright © 2012 Open Geospatial Consortium
To obtain additional rights of use, visit http://www.opengeospatial.org/legal/.

Warning

This document is not an OGC Standard. It is distributed for review and comment. It is subject to change without notice and may not be referred to as an OGC Standard.

Document type:   	OGC® <Publicly Available Best Practice

Document subtype:   	<interface, encoding, application profile, profile>

Document stage:   	Draft

Document language: 	English

Recipients of this document are invited to submit, with their comments, notification of any relevant patent rights of which they are aware and to provide supporting documentation.

Abstract

This document proposes a set of Best Practices and some guidelines for implementing and using the OGC Web Map Service (WMS) to serve maps which are time-dependent or elevation-dependent. In particular, clarifications or restrictions on the use of WMS are defined to allow unambiguous and safe interoperability between clients and servers, both in the context of expert meteorological and oceanographic usage and in other communities using meteorological and oceanographic information in conjunction with their own domains’ data. This Best Practice applies specifically to WMS version 1.3, but many concepts and recommendations herein will be applicable to other versions of WMS or to other OGC services, in particular Web Coverage Service.

Where strict normative conformance has been identified, this is indicated, with reference to the original standard.

Keywords

The following are keywords to be used by search engines and document catalogues:

ogcdoc, WMS, 1.3, web map service, meteorology, oceanography, time, elevation.

Preface

Attention is drawn to the possibility that some of the elements of this document may be the subject of patent rights. The Open Geospatial Consortium shall not be held responsible for identifying any or all such patent rights.

Recipients of this document are requested to submit, with their comments, notification of any relevant patent claims or other intellectual property rights of which they may be aware that might be infringed by any implementation of the standard set forth in this document, and to provide supporting documentation when possible.

Submitting organizations

The following organizations submitted this Document to the Open Geospatial Consortium Inc.

DWD (Deutscher Wetterdienst)

ECMWF (European Centre for Medium-range Weather Forecasts)

Météo-France

Technische Universität Dresden

UK Met Office

US NOAA

US Navy

Submitters

All questions regarding this submission should be directed to the editor or the submitters:

| Name | Company |
| --- | --- |
| Chris Little | UK Met Office |
| Marie-Françoise Voidrot-Martinez | Météo-France |
| Jeff de La Beaujardière | US NOAA |
| Stephan Siemen | ECMWF |

More generally, these Best Practices are the result of discussions within the OGC Meteorology/Oceanography Domain Working Group (MODWG) and the OGC Technical Committee.

# Introduction

The meteorological and oceanographic communities have been exchanging information internationally for at least 150 years and very well understand the importance of geospatial interoperability standards encompassing standardized data formats, interfaces, processes; shared conceptual models and stable, sustainable, maintenance processes and institutions.

Because of the demanding nature of meteorological and oceanographic data processing, the communities have evolved domain specific solutions. As computers have become more powerful, it has become feasible to use general geospatial software for day-to-day operational purposes, and interoperability problems have arisen. There is also an increasing need to combine meteorological and oceanographic with other forms of geospatial data from other domains, in ways convenient for those domains.

This document describes and justifies a set of Best Practices for implementing Web Map Service (WMS) servers and clients to meet the interoperability requirements of the meteorological and oceanographic communities and to allow the economies of using Commercial Off-The-Shelf geospatial software.

# Scope

This document specifically addresses the existing WMS Version 1.3 standard and implementations.

The possibility of re-using these Best Practices for future versions of WMS and other OGC standards is/could be also considered.

This Best Practice assumes that WMS supports only named Layers and Styles, and does not include a mechanism for user-defined symbolization of feature data.

# Conformance

This Standard defines XXXX.

Requirements for N standardization target types are considered:

AAAA

BBBB

Conformance with this standard shall be checked using all the relevant tests specified in Annex A (normative) of this document. The framework, concepts, and methodology for testing, and the criteria to be achieved to claim conformance are specified in the OGC Compliance Testing Policies and Procedures and the OGC Compliance Testing web site.

In order to conform to this OGC™ interface standard, a software implementation shall choose to implement:

Any one of the conformance levels specified in Annex A (normative).

Any one of the Distributed Computing Platform profiles specified in Annexes TBD through TBD (normative).

All requirements-classes and conformance-classes described in this document are owned by the standard identified as Error! Unknown document property name. .

# References

The following normative documents contain provisions that, through reference in this text, constitute provisions of this document. For dated references, subsequent amendments to, or revisions of, any of these publications do not apply. For undated references, the latest edition of the normative document referred to applies.

OpenGIS® Web Map Server Implementation Specification Version 1.3.0.

Date 2006-03-15. http://portal.opengeospatial.org/files/?artifact_id=14416

ISO 8601:2004, Data elements and interchange formats — Information interchange — Representation of dates and times

# Terms and Definitions

This document uses the terms defined in Sub-clause 5.3 of [OGC 06-121r8], which is based on the ISO/IEC Directives, Part 2, Rules for the structure and drafting of International Standards. In particular, the word “shall” (not “must”) is the verb form used to indicate a requirement to be strictly followed to conform to this standard.

For the purposes of this document, the following additional terms and definitions apply.

4.1

client

software component that can invoke an operation from a server

4.2

geographic information

information concerning phenomena implicitly or explicitly associated with a location relative to the Earth [ISO 19101]

4.3

interface

named set of operations that characterize the behaviour of an entity [ISO 19119]

4.4

layer

basic unit of geographic information that may be requested as a map from a server

4.5

map

portrayal of geographic information as a digital image file suitable for display on a computer screen

4.6

operation

specification of a transformation or query that an object may be called to execute [ISO 19119]

4.7

portrayal

presentation of information to humans [ISO 19117]

4.8

request

invocation of an operation by a client

4.9

response

result of an operation returned from a server to a client

4.10

server

a particular instance of a service

4.11

service

distinct part of the functionality that is provided by an entity through interfaces [ISO 14252]

# Abbreviated terms

COTS 		Commercial Off The Shelf software

GIF 		Graphics Interchange Format

GIS 		Geographic Information System

JPEG 		Joint Photographic Experts Group

OGC 		Open GIS Consortium

PNG 		Portable Network Graphics

SVG 		Scalable Vector Graphics

URL 		Uniform Resource Locator

WebCGM 	Web Computer Graphics Metafile

WMS 		Web Map Service

# Conventions

This sections provides details and examples for any conventions used in the document. Examples of conventions are symbols, abbreviations, use of XML schema, or special notes regarding how to read the document.

# Requirements for WMS MetOcean services

This section will highlight requirements WMS services need to fulfill to offer …

WMS 1.3 predefines two dimensions (time and elevation) and offers a generic way to add further dimensions.

- TIME : <Dimension name="time">

GetMap request includes TIME=T

- ELEVATION: <Dimension name="elevation">

GetMap request includes ELEVATION=Z

- Provider-defined "sample dimensions": <Dimension name="something">

GetMap request includes DIM_something=value

## Handling of time

WMS 1.3 specification requirements that time shall be normally be expressed in ISO 8601 format. From this follows:

- Date/time format: ccyy-mm-ddThh:mm:ss.sssZ, to appropriate precision

- Required attribute: units="ISO8601“

- This includes the time zone

Climatological intervals and temporal references will be the subject of future work and may not use strict ISO 8601. Multiple times may be expressed either as a list or as a start/end/interval, as shown in WMS 1.3 Table C.2.

MetOcean DWG Best Practices:

- <Dimension name="time"> always applies to validity time  (of observation or forecast)

- Express each map as a single Layer with 0+ temporal axes

- Avoid multiple independent layers with time encoded in Layer Name.

### WMS Layer with no defined Time

These can be layers of topographic or for climatological normals (e.g. Standard Normals of maximum temperature in Germany for the period between 1961 and 1990).

MetOcean DWG Best Practices:

- Server:

  - Do not declare a TIME value for this layer

  - Avoid inheritance of TIME from parent layers

- Client:

  - TIME may be included in GetMap request

  - TIME in GetMap request is ignored for this layer

* WMO defines normals as "period averages computed for a uniform and relatively long period comprising at least three consecutive 10-year periods".

### WMS Layer with single Time axis

These are any layers with one or more available times along a single time axis.

MetOcean DWG Best Practices:

- Server:

  - TIME axis states time values {Ti}

    - List (T0, T1,... TN) and/or range (T0/T1/ΔT)    [see WMS Table C.2]

  - Recommended attributes:

    - current=TRUE (if data are continually updated)

    - default=Tdefault  (what time will be sent if client does not specify)

    - nearestValue=TRUE (nearest available time will be sent)

  - Optional attributes:

    - multipleValues=TRUE (if allow multiple times in one request)

      - Result is animation or mash-up of multiple times

- Client:

  - TIME is recommended in GetMap request

Figure 1: Decision tree to analyze Time in GetMap request.

### WMS Layer with double Time axis

For this type of services three use cases were developed:

- Numerical model Outputs

A weather forecast model is initialized and run every 6 hours and produces a 5-day forecast with a temporal resolution of 3 hours. There are multiple forecasts for each 3hr interval.

Figure 2: Time parallelogram of numerical weather forecasts.

- Common Alert Protocol (CAP)

A warning is associated with several time information. The CAP standard (CAP =) defines 4 time attributes:

    - Sent: The time and date of the origination of the warning (Mandatory)

    - Effective: The effective time of the information of the warning

    - Onset: The expected time of the beginning of the subject event of the warning

    - Expires: The expiry time of the information of the warning

In several CAP implementations for met warnings, sent time is equal to effective time. The validity time is the period between „onset“ and „expires“. If CAP files with meteorological warnings are produced periodically (e.g. every 5 minutes), then a warning may exist in more than one CAP file. The sent time can be used to distinguish them via a dimension.

- Trajectories

A trajectory is the path that a moving object follows through space as a function of time.  In meteorology trajectories are often computed periodically. Then you have a set of trajectories with different starting times. The start time can be used to distinguish them via a dimension

MetOcean DWG Best Practices:

- Server:

  - <Dimension name=“time"> : validity times

  - <Dimension name=“reference_time"> shall be used for forecasts analysis or initialisation time

  - <Dimension name=“reference_time"> may be used for other meanings if appropriate

  - Server may define additional time axes <something>_time for non-model data.

    - <Dimension name=“sent_time"> reference time for warnings

    - <Dimension name=“start_time"> reference time for trajectories

  - Sending a change request to update the Best Practices in parallel would be appreciated

- Client: TIME and DIM_XXX_TIME are recommended in GetMap request

Figure 3: Decision tree for XXX_Time in GetMap request.

## Handling of elevation

As a reminder these are the general rules of vertical axes (elevation) in WMS 1.3:

–	Each Layer may have 1 ELEVATION axis <Dimension name="elevation">

–	ELEVATION axis must have a well-defined vertical CRS (coord. ref. syst.)

Mandatory attribute : verticalCRSid (label or URL) - see Clause 6.7.5

–	Elevations shall be expressed in units of this CRS

Required attribute : unitSymbol corresponds to these units

–	ELEVATION axis (if present) shall enumerate 1+ available values

–	Multiple elevations may be expressed either as a list or as a min/max/interval, as shown in WMS 1.3 Table C.2.

–	Express each map as a single Layer with 0 or 1 elevation axes

–	Avoid multiple independent layers with elevation encoded in Name.

# <Clauses not Containing Normative Material>

Paragraph

## Clauses not containing normative material sub-clause 1

Paragraph

### Clauses not containing normative material sub-clause 2

Paragraph

# <Clauses containing normative material>

Paragraph

## <Requirement Class A or Requirement A>

Paragraph – intro text. The following table is an example only. Modify as necessary.

| Requirements Class |
| --- |
| http://www.opengis.net/spec/ABCD/m.n/req/req-class-a |
| Target type | Token |
| Dependency | http://www.example.org/req/blah |
| Dependency | urn:iso:ts:iso:19139:clause:6 |
| Requirement | http://www.opengis.net/spec/ABCD/m.n/req/req-class-a/req-name-1 requirement description |
| Requirement | http://www.opengis.net/spec/ABCD/m.n/req/req-class-a req-name-2 requirement description |
| Requirement | http://www.opengis.net/spec/ABCD/m.n/req/req-class-a /req-name-3 requirement description. |

## Requirement Class B or Requirement B

<Example – remove from document> When a WCS server encounters an error while performing a GetCapabilities operation, the server shall return an exception report message as specified in Clause 8 of [OGC 06-121r8]. http://opengis.net/spec/WCS/2.0/core/exception.

# Media Types for any data encoding(s)

A section describing the MIME-types to be used is mandatory for any standard involving data encodings. If no suitable MIME type exists in http://www.iana.org/assignments/media-types/index.html then this section may be used to define a new MIME type for registration with IANA.

Annex A: Conformance Class Abstract Test Suite (Normative)

Conformance class: AAAA (repeat as necessary)

<Example – remove from document>

Annex B: Revision history

| Date | Release | Author | Paragraph modified | Description |
| --- | --- | --- | --- | --- |
| 2012-07-10 | 0.1.0 | CTL | All | First introductory text |

Annex C: Bibliography

The bibliography may include

—	documents that are not publicly available,

—	documents to which only informative reference is made, and

—	documents which have merely served as references in the preparation of the standard

Annex of notes, reminders, etc. To be deleted when complete.

Get reviews from Adrian Custer, Joan Maso, WMS telcos, Jeremy Tandy and co.

DECISION: Intercept WMS 1.3. Make new one for WMS2.0.

Triage features into: stay same, need to change, don’t know

Pick up details and examples from MoD Profile

Legend: problematic

DECISION: MUST support PNG for transparency as a minimum. SVG nice. Same as WMS 1.3

DIMENSIONS

Names and title

Keyword list

Styles?

Queryable layers LATER?

Bounding box

CRS

Scale

Data URL ?

Null/negative responses.

Table 1 UNCHANGED

Table 2 UNCHANGED

Table 3 — The parameters of a GetCapabilities request URL

| Request parameter | Mandatory / optional | Description | Met Ocean Profile |
| --- | --- | --- | --- |
| VERSION=version | O | Request version | M |
| SERVICE=WMS | M | Service type | No change |
| REQUEST=GetCapabilities | M | Request name | No change |
| FORMAT=MIME_type | O | Output format of service metadata | ? |
| UPDATESEQUENCE=string | O | Sequence number or string for cache control | ? |

Table 4 — Use of UpdateSequence parameter UNCHANGED

| Client request UpdateSequence value | Server metadata UpdateSequence value | Server response | Met Ocean profile |
| --- | --- | --- | --- |
| None | any | most recent service metadata | No change |
| Any | none | most recent service metadata | No change |
| equal | equal | Exception: code=CurrentUpdateSequence | No change |
| Lower | higher | most recent service metadata | No change |
| higher | lower | Exception: code=InvalidUpdateSequence | No change |

Table 5 — Relationship between ISO 19128 and ISO 19115 metadata fields

| ISO 19128 layer property | ISO 19115 Metadata element | Relationship |  |
| --- | --- | --- | --- |
| Title | CI_Citation.title | equivalent | Check WMO core Profile |
| Abstract | MD_DataIdentification.abstract | equivalent | Check WMO core Profile |
| Keyword element inKeywordList | MD_TopicCategoryCode | equivalent if “vocabulary” attribute of 19128 <Keyword> element is “ISO 19115:2003”. Other vocabularies are permitted by 19128. | Check WMO core Profile |
| EX_GeographicBoundingBox | EX_GeographicBoundingBox | equivalent | No change |
| CRS | MD_CRS | Value of CRS in 19128 is a text string that identifies a coordinate reference system defined by another authority. Value of MD_CRS in 19115 is a list of projection, ellipsoid and datum identifiers. | ?? |
| BoundingBox | EX_BoundingPolygon | 19128:BoundingBox is strictly a box (lower left and upper right corners in a specified CRS). 19115:EX_BoundingPolygon may be a polygonal boundary. | ?? |
| Attribution | CI_ResponsibleParty | Title element of 19128:Attribution is equivalent to organisationName element of 19115: CI_ResponsibleParty. Other elements of 19128:Attribution have no equivalent in 19115. | Check WMO core Profile |
| Identifier and AuthorityURL | CI_Citation.identifier | The value of 19128:Identifier is equivalent to 19115:CI_Citation.identifier.code. 19128:AuthorityURL contains only the URL of the authority for a namespace, and is equivalent to 19115: CI_Citation.identifier.citation.citedResponsibleParty. contactInfo.onlineResource. 19115 allows a fuller description of the namespace authority. | Check WMO core Profile |
| DataURL | MD_metadata.dataSetURI | equivalent | No change |

Table 6 — Layer attributes

| Attribute | Allowed values | Meaning (0 is default value) | Met Ocean Profile |
| --- | --- | --- | --- |
| queryable | 0, false, 1, true | 0, false: layer is not queryable. 1, true: layer is queryable. | ?? |
| cascaded | 0, positive integer | 0: layer has not been retransmitted by a Cascading Map Server. n: layer has been retransmitted n times. | No change |
| Opaque | 0, false, 1, true | 0, false: map data represents vector features that probably do not completely fill space. 1, true: map data are mostly or completely opaque. | No change |
| noSubsets | 0, false, 1, true | 0, false: WMS can map a subset of the full bounding box. 1, true: WMS can only map the entire bounding box. | No change |
| fixedWidth | 0, positive integer | 0: WMS can produce map of arbitrary width. nonzero: value is fixed map width that cannot be changed by the WMS. | No change |
| fixedHeight | 0, positive integer | 0: WMS can produce map of arbitrary height. nonzero: value is fixed map height that cannot be changed by the WMS. | No change |

Table 7 — Inheritance of Layer properties

| Element | Number | Inheritance | Met Ocean Profile |
| --- | --- | --- | --- |
| Layer | 0+ | no | No change |
| Name | 0/1 a | no | No change |
| Title | 1 | no | No change |
| Abstract | 0/1 | no | No change |
| KeywordList | 0/1 | no | No change |
| Style | 0+ | add | No change |
| CRS | 1+ b | add | No change |
| EX_GeographicBoundingBox | 1 b | replace | No change |
| BoundingBox | 1+ b | replace | No change |
| Dimension | 0+ | replace | No change |
| Attribution | 0/1 | replace | No change |
| AuthorityURL | 0+ | add | No change |
| Identifier | 0+ | no | No change |
| MetadataURL | 0+ | no | No change |
| DataURL | 0/1 | no | No change |
| FeatureListURL | 0/1 | no | No change |
| MinScaleDenominator, MaxScaleDenominator | 0/1 | replace | No change |
| Attributes listed in Table 6 | 0/1 | replace | No change |

a See 7.2.4.6.3 regarding distinction between named and unnamed layers.

b May be 0 only if a value is inherited from an enclosing Layer element; see 7.2.4.6.6 through 7.2.4.6.8

Table 8 — The Parameters of a GetMap request

| Request parameter | Mandatory / optional | Description | Met Ocean Profile |
| --- | --- | --- | --- |
| VERSION=1.3.0 | M | Request version. | No change |
| REQUEST=GetMap | M | Request name. | No change |
| LAYERS=layer_list | M | Comma-separated list of one or more map layers. | No change |
| STYLES=style_list | M | Comma-separated list of one rendering style per requested layer. | No change |
| CRS=namespace:identifier | M | Coordinate reference system. | No change |
| BBOX=minx,miny,maxx,maxy | M | Bounding box corners (lower left, upper right) in CRS units. | No change |
| WIDTH=output_width | M | Width in pixels of map picture. | No change |
| HEIGHT=output_height | M | Height in pixels of map picture. | No change |
| FORMAT=output_format | M | Output format of map. | No change |
| TRANSPARENT=TRUE¦FALSE | O | Background transparency of map (default=FALSE). | ?? |
| BGCOLOR=color_value | O | Hexadecimal red-green-blue colour value for the background color (default=0xFFFFFF). | ?? |
| EXCEPTIONS=exception_format | O | The format in which exceptions are to be reported by the WMS (default=XML). | No change |
| TIME=time | O | Time value of layer desired. | ?? |
| ELEVATION=elevation | O | Elevation of layer desired. | ?? |
| Other sample dimension(s) | O | Value of other dimensions as appropriate. | ?? Add more detail e.g. 2nd time probability threshold |

Table 9 — The Parameters of a GetFeatureInfo Request

| Request parameter | Mandatory / optional | Description | Met Ocean Profile |
| --- | --- | --- | --- |
| VERSION=1.3.0 | M | Request version. | No change |
| REQUEST=GetFeatureInfo | M | Request name. | No change |
| map request part | M | Partial copy of the Map request parameters that generated the map for which information is desired. | No change |
| QUERY_LAYERS=layer_list | M | Comma-separated list of one or more layers to be queried. | No change |
| INFO_FORMAT=output_format | M | Return format of feature information (MIME type). | ?? XML+Schema? |
| FEATURE_COUNT=number | O | Number of features about which to return information (default=1). | No change |
| I=pixel_column | M | i coordinate in pixels of feature in Map CS. | No change |
| J=pixel_row | M | j coordinate in pixels of feature in Map CS. | No change |
| EXCEPTIONS=exception_format | O | The format in which exceptions are to be reported by the WMS (default= XML). | ?? |

B.2 Map CS (CRS:1)

Table B.1 — Definition of map coordinate system

| Element name | Entry | Comment | Met Ocean Profile |
| --- | --- | --- | --- |
| Coordinate system identifier | CRS:1 | See 6.7.2 |  |
| Coordinate system type | Cartesian |  |  |
| Datum identifier | computer display |  |  |
| Datum type | engineering |  |  |
| Coordinate system dimension | 2 |  |  |
| Coordinate system axis name | i |  |  |
| Coordinate system axis direction | east | Some maps, especially over the poles, may not have a well-defined linear axis direction. |  |
| Coordinate system axis unit identifier | pixel |  |  |
| Coordinate system axis name | j |  |  |
| Coordinate system axis direction | south | Some maps, especially over the poles, may not have a well-defined linear axis direction. |  |
| Coordinate system axis unit identifier | pixel |  |  |
| Coordinate system remarks | Origin is in upper left. Axis values are non-negative integers. |  |  |

B.3 Layer CRS using WGS 84 longitude-latitude (CRS:84)

Table B.2 — Definition of Layer CRS using WGS 84 longitude-latitude

| Element name | Entry | Comment | Met Ocean Profile |
| --- | --- | --- | --- |
| Coordinate reference system kind code | 1 | Single (not compound) CRS |  |
| Coordinate reference system identifier | CRS:84 |  |  |
| Coordinate reference system valid area | world |  |  |
| Datum identifier | WGS 84 |  |  |
| Datum type | geodetic |  |  |
| Prime meridian identifier | Greenwich |  |  |
| Prime meridian Greenwich longitude | 0 degree |  |  |
| Ellipsoid identifier | WGS 84 |  |  |
| Ellipsoid semi-major axis | 6378137.0 m |  | ?? Cross check |
| Ellipsoid shape | true |  |  |
| Ellipsoid inverse flattening | 298.257223563 |  | ??Cross check |
| Coordinate system identifier | Geodetic Coordinate System |  |  |
| Coordinate system type | geodetic |  |  |
| Coordinate system dimension | 2 |  |  |
| Coordinate system axis name | longitude | The first (x) axis is longitude in this CRS. |  |
| Coordinate system axis direction | east |  |  |
| Coordinate system axis unit identifier | degree |  |  |
| Coordinate axis minimum value | −180 degrees |  |  |
| Coordinate axis maximum value | 180 degrees |  |  |
| Coordinate system axis name | latitude | The second (y) axis is latitude in this CRS. |  |
| Coordinate system axis direction | north |  |  |
| Coordinate system axis unit identifier | degree |  |  |
| Coordinate axis minimum value | −90 degrees |  |  |
| Coordinate axis maximum value | 90 degrees |  |  |

NOTE CRS:84 is permitted to be used at large scales (>10m/pixel) for describing or requesting map layers in any lon/lat

CRS that is equivalent to within ~1m.

Add something like B.6

Table C.1 — Contents of a dimension element

| Field | Mandatory / optional | Meaning | Met Ocean Profile |
| --- | --- | --- | --- |
| name | M | Attribute stating name of dimensional axis. | No change |
| Units | M | Attribute indicating units of dimensional axis. | No change |
| unitSymbol | O | Attribute specifying symbol. |  |
| Default | O | Attribute indicating default value that will be used if GetMap request does not specify a value. If attribute is absent, then shall respond with a service exception if request does not include a value for that dimension. | M? |
| multipleValues | O | Boolean attribute indicating whether multiple values of the dimension may be requested. 0 (or “false”) = single values only; 1 (or “true”) = multiple values permitted. Default = 0. |  |
| nearestValue | O | Boolean attribute indicating whether nearest value of the dimension will be returned in response to a request for a nearby value. 0 (or “false”) = request value(s) must correspond exactly to declared extent value(s); 1 (or “true”) = request values may be approximate. Default = 0. |  |
| current | O | Boolean attribute valid only for temporal extents (i.e. if attribute name="time"). This attribute, if it either 1 or “true”, indicates (a) that temporal data are normally kept current and (b) that the request parameter TIME may include the keyword “current” instead of an ending value (see C.4.1). Default = 0. | M? |
| Extent | M | Text content indicating available value(s) for dimension. | No change |

# Footnotes

www.opengeospatial.org/cite

# Comments

Do we have any of this?

Is this really true? I think Styles, whether named or via SLD, are orthogonal to the Time and Elevation discussion. If not, we need to identify exactly where there is mixing and perhaps eliminate it.

This caused most feedback at OGCTC and EGOWS. This can be very dangerous because there is no feedback to the client which time has been sent!

Is this valid if we want one layer at a time?

There were many comments that the HTTP response header would be hard to implement in clients.

Do we need the use cases here?